## Slide 1: Codeerzeugung für eingebettete Prozessoren
(WS 2001/2002)
Dr.-Ing. Daniel Kästner
Lehrstuhl für Programmiersprachen und Übersetzerbau (Prof. Wilhelm)
fon: +49-681-302-5589
kaestner@cs.uni-sb.de

## Slide 2: Organisatorisches
Vorlesung: Do, 14-16
Übungen:
Vorlesungsfolien, Literaturlisten, Aktuelles unter
http://www.cs.uni-sb.de/~kaestner/CG0102.html
Folien auf Englisch. Einwände?

## Slide 3: Today
What is an embedded system?
What do embedded applications look like?
What makes embedded processors special?
Why is the code generation problem important?
Why is it a problem?

## Slide 4: Embedded Systems: Definition
Embedded processors are embedded in a physical environment and interact with it for measuring or controlling purposes.
Characteristics of embedded applications:
  complex interaction with environment (non-deterministic, contineous behavior; signals arrive at enormeous rates; signal processing and information filtering become key issues)
  high dependability requirements
  often real-time processing required

## Slide 5: Special Case: Real-Time Systems
In a real-time system, the correctness not only depends on the logical results but also on the timing of the applications.
Definition (Oxford Dictionary of Computing): Any system in which the time at which output is produced is significant. This is usually because the input corresponds to some movement in the physical world, and the output has to relate to that same movement. The lag from input time to output time must be sufficiently small for acceptable timeliness.

## Slide 6: Special Case: Real-Time Systems
Distinction:
  Hard real-time system: It is vital that the system satisfies the timing condition. Failure results in catastrophic consequences, e.g. the loss of lifes. Examples: flight control software, airbag control.
  Soft real-time system: It is desirable that the system satisfies the timing conditions; otherwise the functioning of the system is negatively affected. Example: MP3-Player, telephone software.

## Slide 7: Design of Embedded Systems: Goal Conflict
High performance requirements
Increasing software complexity
High dependability
Low cost
Low power consumption
Short product and development cycles

## Slide 8: Software Complexity
The amount of control software in consumer products is doubling roughly every 2 years [B98].
ROM Size/Year | 1985 | 1990 | 1995 | 1998
High-end TV | 10K | 100K | 800K | 1.4M
Hifi Audio Set | - | 10K | 100K | 256K
VCR | 10K | 100K | 800K | 1.2M
GSM phone | - | - | 1M | 2M
Set-top box | - | 2K | 128K | 1M
Shaver | - | 2K | 16K | 16K

## Slide 9: Market for Embedded Processors
Market for embedded processors estimated at almost $50 billion (109) in 1997; annual growth estimated at 35% per year (Micrologic Research).
Worldwide semiconductor sales total $204 billion in 2000 (Semiconductor Industry Association).
Embedded chips account for more than 90 % of all silicon processors sold [Leibson(Embedded Processor Forum), 2001]
The global market for general-purpose DSPs grew 25.5% to $4.4 billion in 1999 [Tempe Research Company].

## Slide 10: Today
What is an embedded system?
What do embedded applications look like?
What makes embedded processors special?
Why is the code generation problem important?
Why is it a problem?

## Slide 11: Examples: Consumer Electronics
AV-R Receivers (e.g. Analog Devices SHARC)
Smart Pen
CD-player, DVD-player, MP3-player
Organizer, PDAs
Washing machines, microwave ovens, ...
PC peripherals (hard disk control, graphic cards, ...)

## Slide 12: Examples: Telecommunications
Devices:
  Cell phones
  ISDN phones, fax
  Answering machines, etc
DSP-Applications:
  voice and data compression
  echo reduction
  signal multiplexing
  filtering
Notes: GSM Phone – Operation
Initialization of hardware
User identification
Locate network
Announcement to network
Lower transmission power
Download all SMS messages
Voice call connection:
user types number
  number is sent to PSTN (Public switched telephone network), which translates it into route
  all swithces in the route are connected
  charging is established
  If the user moves from one location to another, the call is handed over to another network
  At the end the call is disconnected and the user is billed.

## Slide 13: Examples: Automotive
An average passenger car has roughly the equivalent of six Pentium processors; currently there are up to 100 microprocessors per car.
Engine control
Active suspension
Air-conditioning
Airbag
Navigation systems (GPS)
Sound system, active noise cancellation
...

## Slide 14: Examples: Avionics and Healthcare Technology
Pilot information systems
Fly-by-wire
Security control
Diagnostic imaging (Computed Tomography, Magnetic Resonance Imaging, ultrasound, etc)
Electrocardiagram analysis
Medical image storage/retrieval
Notes: Computed tomography: X-rays from many directions are passed through the section of the patient's body being examined. Instead of simply forming ijmages with the detected X-rays, the signals are converted into digital data and stored in a computer. This information is then used to calculate images that appear to be slicesx through the body.
Magnetic resonance imaging uses magnetic fields in conjunction with radio waves to probe the interior of the human body. Properly adjusting the strength and frequency of the fields cause the atomic nuclei in a localized region of the body to resonate between quantum energy states. This resonance results in the emission of a secondary radio wave, detected with an antenna placed near the
body. The strength and other haracteristics of this detected signal provide information about the localized region in resonance. Adjustment of the magnetic field allows the resonanc region to be scanned throughout the body, mapping the internal structure. MRI can provide excellent discrimination between different types of soft tissure, information about physiology such as blood flow through artieries.

## Slide 15: Today
What is an embedded system?
What do embedded applications look like?
What makes embedded processors special?
Why is the code generation problem important?
Why is it a problem?

## Slide 16: Classification of Microprocessors
Specialization
Requirements:
  high performance
  low cost
  low power consumption

## Slide 17: Architectural Valuation
[Campbell, Northrop Grumman Corporation, 1998]
More efficient architectures will use less energy to complete the same task on the same generation CMOS solid state technology
Power consumption
  C : Capacitance
  V : CPU Core Voltage
  f : CPU clock frequency
  N : Number of gates changing state

## Slide 18: Architectural Valuation
Observations:
  Higher performance by increasing the clock frequency does not change the performance per power ratio
  A voltage decrease improves performance per power non-linearly

## Slide 19: Architectural Valuation
Architectural specialization as a measure for how well the architecture fits a given target application.
Estimation of architectural specialization: Performance per power.

## Slide 20: Comparion of Performace Per Power Ratios

## Slide 21: DSP vs. GPP: Some Figures

## Slide 22: Focus: Digital Signal Processors
Programmable microprocessors specialized for applications of digital signal processing.
Characteristics:
  Multiply-accumulate units
  Multiple access memory architecture
  Specialized addressing modes: auto-modify addressing, circular addressing, bit-reverse addressing
  Residual control / predicated execution
  Hardware loops / zero-overhead loops
  Restricted interconnectivity between registers and functional units
  Encoding restrictions

## Slide 23: Today
What is an embedded system?
What do embedded applications look like?
What makes embedded processors special?
Why is the code generation problem important?
Why is it a problem?

## Slide 24: Classical DSPs: Analog Devices ADSP-2106x SHARC

## Slide 25: Multimedia DSPs: TriMedia TM1000 (1)

## Slide 26: Multimedia DSPs: TriMedia TM1000 (2)
Generic VLIW Architecture

## Slide 27: DSP & Microcontroller: Infineon TriCore

## Slide 28: Intel IA64
Block diagram of Intel Intanium.

## Slide 29: Today
What is an embedded system?
What do embedded applications look like?
What makes embedded processors special?
Why is the code generation problem important?
Why is it a problem?

## Slide 30: Compiler Structure
Input
program
Intermediate representation
Assembly or machine code
void main(void) {
int a, b, c;
c=a+b;
}
r1=dm(i7, m7)
r2=pm(i8, m8)
r3=r1+r2
Frontend
Backend
Frontend
Syntactic and semantic analysis
Backend
Code generation Code optimization

## Slide 31: Code Selection, Register Allocation, and Instruction Scheduling
c=a+b;
load adr(a)
add
load adr(b)
store adr(c)
Code selection
Instruction scheduling
b
c
a
r1=load adr(a)
r3=add r1, r2
r2=load adr(b)
store adr(c), r3
r1=load adr(a) || r2=load adr(b)
store adr(c), r3
r3=add r1, r2
Register allocation

## Slide 32: Phase Coupling Problem
d1=s1*s1;
d2=s1+s2;
r3=r1*r1
store r3
r3=r1+r2
store r3
r3=r1*r1, r4=r1+r2
store r3
store r4
Optimize number of used registers
Optimize code speed and size

## Slide 33: The Code Generation Problem
Instruction scheduling, register allocation and code selection are NP complete problems.
In classical approaches they are addressed by heuristic methods in separate phases.
Unfortunately, all the code generation phases are interdependent, i.e. decisions made in one phase may impose restrictions to the other phases.
Thus: often suboptimal combination of suboptimal partial results.
Moreover: specific/irregular hardware features not well covered by standard code generation methods.

## Slide 34: The DSPStone Study
Evaluation of the performance of DSP compilers and joint compiler/processor systems.
Evaluated: Analog Devices ADSP2101, AT&T DSP1610, Motorola DSP56001, NEC mPD77016, TI TMS320C51.
Hand-crafted assembly code is compared to the compiler-generated code.
Result: overhead between 100% and 1000% of compiler-generated code is typical !

## Slide 35: Compiling for DSPs
Code quality of traditional high-level language compilers is not satisfactory.
Thus: Assembly programming.

## Slide 36: Case Study: Infineon TriCore
Zero-Overhead Loops
SIMD Instructions
Auto-modify addressing
6 times faster!
(execution in SRAM)
C code (FIR Filter):
int i,j,sum;
for (i=0;i<N-M;i++) {
sum=0;
for (j=0;j<M;j++) {
sum+=array1[i+j]*coeff[j];
}
output[i]=sum>>15;
}
Compiler-generated code (gcc):
.L21: add %d15,%d3,%d1
addsc.a %a15,%a4,%d15,1
addsc.a %a2,%a5,%d1,1
mov %d4,49
ld.h %d0,[%a15]0
ld.h %d15,[%a2]0
madd %d2,%d2,%d0,%d15
add %d1,%d1,1
jge %d4,%d1,.L21
Hand-written code (inner loop):
_8: ld16.w d5, [a2+]
ld16.w d4, [a3+]
madd.h e8,e8,d5,d4ul,#0
loop a7,_8

## Slide 37: Overview of Lecture
Embedded systems and digital signal processing.
Hardware characteristics of embedded processors.
Code generation methods for specific hardware features.
Code generation methods for the phase coupling problem.