## Slide 1: DSP/MCU: Infineon TriCore

## Slide 2: Infineon TriCore
RISC-based 32-bit load/store architecture with Harvard architecture.
64-bit program memory bus between instruction fetch unit and program memory (fetch of up to 4 instructions).
128-bit data memory bus. Transfer of two data and two address registers in one clock cycle.

## Slide 3: Infineon TriCore
32 general purpose registers separated in 16 address registers (A0-A15) and 16 data registers (D0-D15).

## Slide 4: Infineon TriCore
The Core Special function registers (CSFRs) control the operation of the core and provide status information: program state information, context management, interrupt and trap control, etc.
The CSFRs are mapped in the memory address space.
Memory space:
  address width: 32 bit
  4GB physical address space, divided into 16 sements of 256MB
  4GB virtual address space , divided into 16 sements of 256MB
  First 16 KB of each segment can be accessed with absolute addressing

## Slide 5: Infineon TriCore
Addressing Mode | Syntax | Effective Address
Absolute | const | constant
Base + short offset | [An]offset10 | A[n] + sext(offset10)
Base + long offset | [An]offset16 | A[n] + sext(offset16)
Pre-increment | [+An]offset10 | A[n] + sext(offset10)
Post-increment | [An+]offset10 | A[n]
Circular | [An+c] | A[n] + A[n+1][15:0]
Bit-reverse | [An+r] | A[n] + A[n+1][15:0]

## Slide 6: Infineon TriCore
Task: independent thread of control. Its state is defined by the task's context.
Context switches occur on interrupts, traps and function calls.
Upper context registers are automatically saved upon context switch in dedicated context save areas. They serve as non-volatile registers in function calling.
Lower context registers can be used to pass parameters to functions.

## Slide 7: Infineon TriCore
Instructions are 32-bit wide; some instructions also have short 16-bit forms.
16-bit instructions use one of the following methods to limit the encoding width:
  combined source and destination operands
  implicit source, destination, or base address operand
  small constants, short branch displacements
Instructions for addition, subtraction, multiplication, multiply and accumulate, division, and shifting.

## Slide 8: Infineon TriCore
Bit field instructions, e.g. EXTR D1, D2, 3, 8
Bit instructions, e.g. AND.T, and combined bit operations, e.g. AND.OR.T
Control flow instructions: branches, loops, context save and restore, calls and returns.
Zero-overhead loops: .L23 mov.a a15, 149 ld.h d8,[a14+] add d15,d8 loop a15, .L23

## Slide 9: Infineon TriCore
Branch prediction:
  if the branch is a 16-bit instruction (backward or forward), the branch is predicted as taken.
  if the branch is a 32-bit instruction and is a backward jump, it is predicted as taken.
  if the branch is a 32-bit instruction and is a forward jump, it is predicted as not taken.
Conditional instructions: SEL, CMOV, CADD, CSUB. Beispiel: D3 = ((d4 != 0) ? d1 : d2 implementiert durch SEL d3, d4, d1, d2

## Slide 10: Infineon TriCore
Fractional arithmetic:
  Number a=(am+n-1, ..., a0) in mqn-format: Example: 2.14-format:
  Frequently used: 1q31-format (Q31), 1q15 (Q15), 2q14 (Q14)
  Addition of q-format numbers: input format must be identical; then output format is the same as input format.
  Multiplication: <a q b> * <c q d > -> <(a+c)> q <(b+d)>
  Characterized by the suffix .Q to the instruction mnemonic.

## Slide 11: Infineon TriCore
SIMD packed arithmetic:
  Packed arithmetic instructions partition a 32-bit word into several identical objects.
Halfword 0
Halfword 1
Halfword0
Halfword1
Destination0
Destination1
OP

## Slide 12: Infineon TriCore
SIMD packed arithmetic:
  Packed arithmetic instructions partition a 32-bit word into several identical objects.
  Two packed formats: 32-bit word divided into
    two 16-bit halfword values (.H/.HU)
    four 8-bit byte values (.B/.BU)
  Load/store of packed values by normal load/store instructions.
  Packed objects can be manipulated in parallel: addition, subtraction, multiplication, absolute value.
  Example: ADD.H D1, D2, D3

## Slide 13: Infineon TriCore
Complex instructions, e.g. : maddsum.h E2, E3, D0, D1UL, 1  E2[63:0] = E3[63:0] + (((D0[31:16] * D1[31:16])<<1) - ((D0[15:0] * D1[15:0] )<<1))

## Slide 14: Infineon TriCore
Pipeline Mechanism: two major pipelines with four stages each (integer and load/store pipeline), and one minor pipeline for loop control.

## Slide 15: Infineon TriCore
Instruction Timing:
  If an LS instruction follows an IP instruction, both are executed in one clock cycle, except in case of MAC instructions and some dual pipeline instructions.
  The execution time of instructions ranges from 1 to 4 clock cycles (best case assumption: no cache misses, no pending loads/stores).
  LOOP/LOOPU instructions take one cycle on first execution of the loop and one cycle on loop exit; during the execution of the loop they do not take a cycle.
  Branches:
    correctly predicted as taken: 2 cycles
    correctly predicted as not taken: 1 cycle
    mispredicted: 3 cycles

## Slide 16: VLIW: TriMedia TM1000 (1)

## Slide 17: VLIW: TriMedia TM1000 (2)
Generic VLIW Architecture

## Slide 18: TriMedia TM1000
Media processor for real-time processing of audio, video, graphics and communication.
DSPCPU: 100 MHz VLIW core CPU; described in the following.
32-bit VLIW processor with 128 general purpose registers and 27 functional units.
16 KB dual-ported data cache and 32 KB instruction cache, both 8-way set-associative with 64 KB block size.
Load/store architecture.

## Slide 19: TriMedia TM1000
Instruction set is composed of RISC-like operations, multimedia and DSP operations (SIMD; e.g. ifir)
Each instruction word is composed of 5 microoperations.

## Slide 20: TriMedia TM1000
Execution time of operations is between 1 and 17 clock cycles.
The packing of operations into instructions (assignment of operations to issue slots of the instruction word) is restricted:
  E.g. no more than two load/store operations can be packed into a single instruction.
  No more than 5 results can be written during any one cycle.
Predicated execution: each operation can optionally be guarded. The operation is executed depending on the value of the general-purpose register specified as guard operand.

## Slide 21: TriMedia TM1000
Feasible issue slot combinations:

## Slide 22: TriMedia TM1000
Example code sequence:
(* cycle 0 *)
IF r1 iaddi(0x2) r0 -> r38, IF r1 isubi(0x4) r0 -> r7,
IF r1 isubi(0x3) r0 -> r8, IF r1 isubi(0x2) r0 -> r36,
IF r1 isubi(0x1) r0 -> r37;
(* cycle 1 *)
IF r1 iaddi(0x3) r0 -> r39, IF r1 uimm(0x190) -> r34,
IF r1 iaddi(0x8) r0 -> r35, IF r1 h_st8d(0) r7 r6,
IF r1 h_st8d(4) r0 r6;

## Slide 23: EPIC: IA64 - Intel Itanium
Block diagram of Intel Intanium.

## Slide 24: IA-64 Architecture
Support for
  branch prediction (minimize the cost of branches),
  predicated execution (remove branches),
  control speculation and data speculation (reduce memory latency effects)
  cache hints (compiler prediction of spatial or temporal locality of the memory area being accessed; can be used for placement of cache lines in the cache hierarchy by the processor)
Register sets:
  128 64-bit general purpose registers: GR0-GR127
  128 80-bit floating-point registers: FR0-FR127
  64 1-bit predicate registers: PR0-PR63
  8 64-bit branch registers: BR0-BR7
  features: register stack and rotating registers

## Slide 25: IA-64 Architecture
GPR0-31 are termed the static general purpose registers.
General purposse registers 32-127 are termed the stacked general purpose registers. The stacked general purpose registers are made available to a program by allocating a register stack frame consisting of a programmable number of local and output registers.
Similarly for the floating-point registers.
Deferred speculative exceptions are recorded with a special register value called NaT (Not a Thing).
Predicated registers 0-15 are the static predicate registers; 16-63 the rotating predicate registers, used in modulo scheduling.
The CFM is the Current Frame Marker that describes the state of the IA64-general register stack. Each general register stack frame is associated with a frame marker. It specifies the size of the stack frame, the size of locals, rotating, and the register rename bases.
The Loop Count Register (LC) is a 64-bit register used in counted loops. LC is decremented by counted-loop type branches.

## Slide 26: IA-64 Architecture
Each IA-64 instruction is categorized into 6 types and may be executed on one or more execution unit types.
4 functional unit categories:
  I unit (integer)
  F unit (floating-point)
  M unit (memory)
  B unit (branch)
6 microoperation categories:
  Integer ALU (A-type) executed on M- or I units
  Non-ALU Integer (I-type) executed on I units
  Memory (M-type) executed on M units
  Floating-point (F-type) executed on F units
  Branch (B-type) executed on B units
  Extended (L/X-type) executed on I- or B units

## Slide 27: IA-64 Architecture
The IA-64 defines 128-bit long instruction words (called bundles) consisting of three 41-bit microoperations and a 5-bit template field. Multiple bundles can be issued per clock cycle (number is defined by implementation).
Template field:
  helps decode and route instructions
  indicates the location of stops that mark the end of groups of microoperations that can execute in parallel
Dispersal: process of sending instructions to functional units.
instruction slot 1
t(5)
instruction slot 2
instruction slot 0

## Slide 28: IA-64 Architecture
There are 12 basic bundle types: MII, MI_I, MLX, MMI, M_MI, MFI, MMF, MIB, MBB, BBB, MMB, MFB. Each basic type has two versions, one with a stop after the third slot and one without.
An instruction group is a sequence of instructions starting at a given bundle address up to the first stop, taken branch, break.b instruction fault or illegal operation fault.
Instruction groups can extend over an arbitrary number of bundles and are determined by the location of stops in assembly code.
Instruction execution phases:
  fetch: read the instruction from memory
  read: read architectural state
  execute: perform the specified operation
  update: update architectural state, if necessary

## Slide 29: IA-64 Architecture: Bundling and Dispersal on Itanium

## Slide 30: IA-64 Architecture
Between instruction groups: instructions behave as though read accesses occur after the update of all instructions from the previous group.
Within instruction groups: instructions behave as though
  memory read accesses occurred after the update of the memory of all prior instructions in the same group.
  register read accesses occurred before the update of the register state by any instruction (prior or later) in the same instruction group – with the exception of some dependence requirements (see next slide).

## Slide 31: IA-64 Architecture
Register dependencies: Within an instruction group, read-after-write (RAW) and write-after-read (WAR) register dependencies are not allowed (with respect to explicit and implicit register accesses), except for some special cases. Write-after-read register dependencies (WAR) are allowed, except for some special cases.
If the program violates the dependency rules within an instruction group, processor behavior is undefined.
Memory dependencies: Within an instruction group, RAW, WAW, and WAR memory dependencies are allowed. A load will observe the results of the most recent store to the same memory address.

## Slide 32: IA-64 Architecture

## Slide 33: IA-64 Architecture
Register Stack Behavior on Procedure Call and Return
When a br.call is executed, the CFM is copied to the previous frame marker field PFM in the Previous Function State application register (PFS), and the callee's frame is created as follows:
The stacked registers are renamed such that the first register in the caller's output area becomes GR32 for the caller.
The size of the local area is set to 0.
The size of the callee's frame (sof) is set to the size of the caller's output area (sof-sol).
sof: size of frame
sol size of locals

## Slide 34: IA-64 Architecture
Compare instructions and predication:
  A compare instruction tests for a single specified condition and generates a boolean result which is written to predicate registers. The predicate registers can be used as conditions for conditional branches and as qualifying predicates for predication.
  Most compare instructions set two predicate registers.
  Compare instructions can have 5 types: Normal, Unconditional, AND, OR, or DeMorgan. The type defines how the instruction writes its target predicate registers.
  AND, OR, and DeMorgan types are termed "parallel" compare types since they allow multiple simultaneous compares to target a single predicate register.

## Slide 35: IA-64 Architecture
Compare Types:

## Slide 36: IA-64 Architecture
Parallel compare instructions: if (r1==1 || r2==1 || r3==1 || r4==1) then s; cmp.ne p1,p0 = r0, r0;; //init cmp.eq.or p1,p0 = 1,r1 cmp.eq.or p1,p0 = 1,r2 cmp.eq.or p1,p0 = 1,r3 cmp.eq.or p1,p0 = 1,r4;; (p1) s

## Slide 37: IA-64 Architecture
Speculation: premature execution of an operation
  conditions:
    low probability of required recovery
    enhancement of instruction-level parallelism by speculative execution.
Control speculation: Execution of an operation before the branch which guards it.
Data speculation: Execution of a memory load prior to a store that precedes it in the operation sequence and that may alias with it.

## Slide 38: IA-64 Architecture
(p1) br.cond label
ld8 r4=[r3];;
add r4=8,r4;;
ld8.s r4=[r3];;
// ...
(p1) br.cond label;;
chk.s r4, recovery;;
back: add r4=8,r4;;
// ...
recovery:
ld8 r4=[r3];;
br back;;
Control speculation:
Assumption: no other uses of r4; otherwise we would have control and data speculation.
Problematic: exception handling. Since the speculative instruction sequence may not be required by the program, no exceptions encountered that would be visible to the program can be signalled until it is determined that the control flow does require the execution of this instruction sequence.
When an exception is deferred by an instruction, a special token is written into the target registers to indicate the existence of a deferred exception in the program.
Deferred exception tokens propagate through the program. A speculative instruction that reads a register containing a deferred exception token will propagate a deferred exception token into its target. Thus a chain of instructions can be executed speculatively. If a deferred exception token is found, then the speculative calculation was unsuccessful and must be redone.
In this case, the chk.s instruction branches to the a new address -> recovery code.

## Slide 39: IA-64 Architecture
Data Speculation:
//...
st8 [r4]=r12
ld8 r6=[r8];;
add r5=r6,r7;;
st8 [r18]=r5
ld8.a r6=[r8];;
// ...
add r5=r6,r7;;
// ...
st8 [r4]=r12
chk.a.clr r6, recovery
back: st8 [r18]=r5
// ...
recovery:
ld8 r6=[r8];;
add r5=r6,r7
br back;;
An ambiguous memory dependence is said to exist between a store (or any operation that may update memory state) and a load when it cannot be statically determined whether the load and store might access overlapping regions of memory.
When an advanced load is xecuted, it allocates an entry in the Advanced Load Address Table (ALAT). Later, when the corresponding check is executed, the presence of an entry indicates that the data speculation succeeded; otherwise the speculation failed and one of two kinds of compiler-generated recovery is performed:
The check load instruction (ld.c) is used for recovery, when the ohly instruction scheduled before a store that is ambiguous relative to the advanced load is the load itself. The check load searches the ALAT for a matching entry. If one is found, speculation has been successful, otherwise the check load reloads the correct value from memory.
-The advanced load check (chk.a) is used when an advanced load and several instructions that depend on the loaded value are scheduled before a store that is ambiguous relative to the advanced load. If the speculation was not successful, the chk.a branches to compiler-generated recovery code.
When memory state is changed, it is checked whether there are overlaps of memory regions of ALAT entries. Overlapping ALAT entries are removed.