## Slide 1: IA-64 Architecture
Review of bundling and dispersal.
Review of control and data speculation.
Intel Itanium.

## Slide 2: IA-64 Architecture
The IA-64 defines 128-bit long instruction words (called bundles) consisting of three 41-bit microoperations and a 5-bit template field. Multiple bundles can be issued per clock cycle (number is defined by implementation).
Template field:
  helps decode and route instructions
  indicates the location of stops that mark the end of groups of microoperations that can execute in parallel
Dispersal: process of sending instructions to functional units.
instruction slot 1
t(5)
instruction slot 2
instruction slot 0

## Slide 3: IA-64 Architecture: Bundling and Dispersal on Itanium

## Slide 4: IA-64 Architecture
Between instruction groups: instructions behave as though read accesses occur after the update of all instructions from the previous group.
Within instruction groups: instructions behave as though
  memory read accesses occurred after the update of the memory of all prior instructions in the same group.
  register read accesses occurred before the update of the register state by any instruction (prior or later) in the same instruction group – with the exception of some dependence requirements (see next slide).

## Slide 5: IA-64 Architecture
Register dependencies: Within an instruction group, read-after-write (RAW) and write-after-read (WAR) register dependencies are not allowed (with respect to explicit and implicit register accesses), except for some special cases. Write-after-read register dependencies (WAR) are allowed, except for some special cases.
If the program violates the dependency rules within an instruction group, processor behavior is undefined.
Memory dependencies: Within an instruction group, RAW, WAW, and WAR memory dependencies are allowed. A load will observe the results of the most recent store to the same memory address.

## Slide 6: IA-64 Architecture

## Slide 7: IA-64 Architecture
(p1) br.cond label
ld8 r4=[r3];;
add r4=8,r4;;
ld8.s r4=[r3];;
// ...
(p1) br.cond label;;
chk.s r4, recovery;;
back: add r4=8,r4;;
// ...
recovery:
ld8 r4=[r3];;
br back;;
Control speculation:
Assumption: no other uses of r4; otherwise we would have control and data speculation.
Problematic: exception handling. Since the speculative instruction sequence may not be required by the program, no exceptions encountered that would be visible to the program can be signalled until it is determined that the control flow does require the execution of this instruction sequence.
When an exception is deferred by an instruction, a special token is written into the target registers to indicate the existence of a deferred exception in the program.
Deferred exception tokens propagate through the program. A speculative instruction that reads a register containing a deferred exception token will propagate a deferred exception token into its target. Thus a chain of instructions can be executed speculatively. If a deferred exception token is found, then the speculative calculation was unsuccessful and must be redone.
In this case, the chk.s instruction branches to the a new address -> recovery code.

## Slide 8: IA-64 Architecture
Data Speculation:
//...
st8 [r4]=r12
ld8 r6=[r8];;
add r5=r6,r7;;
st8 [r18]=r5
ld8.a r6=[r8];;
// ...
add r5=r6,r7;;
// ...
st8 [r4]=r12
chk.a.clr r6, recovery
back: st8 [r18]=r5
// ...
recovery:
ld8 r6=[r8];;
add r5=r6,r7
br back;;
An ambiguous memory dependence is said to exist between a store (or any operation that may update memory state) and a load when it cannot be statically determined whether the load and store might access overlapping regions of memory.
When an advanced load is xecuted, it allocates an entry in the Advanced Load Address Table (ALAT). Later, when the corresponding check is executed, the presence of an entry indicates that the data speculation succeeded; otherwise the speculation failed and one of two kinds of compiler-generated recovery is performed:
The check load instruction (ld.c) is used for recovery, when the ohly instruction scheduled before a store that is ambiguous relative to the advanced load is the load itself. The check load searches the ALAT for a matching entry. If one is found, speculation has been successful, otherwise the check load reloads the correct value from memory.
-The advanced load check (chk.a) is used when an advanced load and several instructions that depend on the loaded value are scheduled before a store that is ambiguous relative to the advanced load. If the speculation was not successful, the chk.a branches to compiler-generated recovery code.
When memory state is changed, it is checked whether there are overlaps of memory regions of ALAT entries. Overlapping ALAT entries are removed.

## Slide 9: IA-64 Architecture
Multimedia instructions supporting packed arithmetic: a general purpose register is considered as concatenated of 8 8-bit, 4 16-bit, or 2 32-bit elements. Operations:
  parallel modulo addition (padd), parallel modulo subtraction (psub), parallel compare (pcmp), etc.
  Data arrangement: interleave odd elements from both sources (mix.l), convert from larger to smaller elements with signed saturation (pack.uss), etc.
Integer (fixed-point) multiply is executed in the floating-point unit (multiply/accumulate). Example: xma f1=f3, f4, f2 computes f1:=f2+f3*f4.

## Slide 10: Intel Itanium
First IA-64 implementation.
Functional units:
  2 M-type
  2 I-type
  2 F-type
  3 B-type
All functional units are fully pipelined.
Functional units of the same type are not identical; seldomly used operations usually can only be executed on the first unit of each type.

## Slide 11: Intel Itanium
Dispersal window contains two bundles allowing up to 6 microoperations to be issued in one clock cycle, among which at most 2 I-type, 2 M-type, 2 F-type, 3 B-type operations.
The functional unit a microoperation is executed by is determined by its type and its position in the bundle.
Execution time:
  1-2 cycles for most integer operations
  2-7 cycles for F-type operations
10-stage pipeline, divided into two parts:
  the 3-stage front end reads the instruction stream
  the 7-stage main pipeline executes the instructions
  front end and main pipeline are decoupled; they are connected by a FIFO buffer that can contain up to 8 bundles.

## Slide 12: Orientation
Embedded systems: Application areas and characteristics.
Digital signal processing: important concepts and algorithms.
Real-life hardware architectures for embedded applications:
  Analog Devices ADSP-2106x SHARC
  Infineon TriCore
  Philips TriMedia TM1000
  Intel IA-64 Architecture & Intel Itanium (currently used for GPP)
Today:
  Summary of features of embedded processors
  Basics of code generation.

## Slide 13: Characteristics of DSPs
Multiply-accumulate units: multiplication and accumulation in a single clock cycle (vector products, digital filters, correlation, fourier transforms, etc)
Multiple-access memory architectures for high bandwidth between processor and memory
  Goal: throughput of one operation per clock cycle.
  Required: several memory accesses per clock cycle.
  Separate data and program memory space: harvard architecture.
  Multiple memory banks
  arithmetic operations in parallel to memory accesses. But often irregular restrictions.

## Slide 14: Characteristics of DSPs
Specialized addressing modes:
  linear addressing mode: addition/subtraction of offset to/from base address, often with auto-modify (pre-/post increment/decrement)
  circular addressing: address results from incrementing an address register and taking the remainder of the division of this value by a constant.
  bit-reverse addressing: carry bits are propagated in bit-reverse order (-> FFT)

## Slide 15: Characteristics of DSPs
Branches depending on control bits: early branch detection allowing for small interlock penalties in combination with typically short pipelines
Residual control: execution behavior depends on specific control bits set by a preceding instruction.
Predicated/guarded execution: instruction execution depends on the value of explicitly specified bit values or registers.
Increasingly: SIMD instructions for packed arithmetic (multimedia applications).

## Slide 16: Characteristics of DSPs
Hardware loops / zero overhead loops: no explicit loop counter increment/decrement, no loop condition check, no branch back to top of loop
Restricted interconnectivity between registers and functional units -> more severe phase coupling problems.
Complex instructions with specific functionality, typical for the application area.
Strongly encoded instruction formats: a throughput of one instruction per clock cycle requires one instruction to be fetched per cycle. Thus each instruction has to fit in one memory word -> reduction of bit width of the instruction. Techniques:

## Slide 17: Characteristics of DSPs
  Techniques for reducing the instruction width:
  Reducing the number of addressing modes. Example: immediate memory accesses restricted to a small set of instructions.
  Restricting the set of source and destination operands: short addressing modes for elements of certain register groups, implied operands.
  Mode bits, for example a single shift instruction that performs arithmetic or logical shifts depending on a control bit in a mode register.
  Consequence: Increased irregularity of the instruction set – but reduction of processor and system cost and increased individual instruction performance.

## Slide 18: Characteristics of DSPs
Overall consequence:
  Irregularity
  Severe phase coupling problems
  Need for specialized algorithms

## Slide 19: Compiler Structure
Input
program
Intermediate representation
Assembly or machine code
void main(void) {
int a, b, c;
c=a+b;
}
r1=dm(i7, m7)
r2=pm(i8, m8)
r3=r1+r2
Frontend
Backend
Frontend
Syntactic and semantic analysis
Backend
Code generation Code optimization

## Slide 20: Detailed Compiler Structure
Source (Text)
Syntax Analysis
Tokenized Program
Syntax Tree
Decorated Syntax Tree
Intermediate Representation
Lexical Analysis
Semantic Analysis
High-Level Optimizations
Code Generation
Machine Program

## Slide 21: Lexical Analysis (Scanning & Screeing)
Input: Program text as sequence of characters. Output: Program text as sequence of symbols (tokens).
Read Input file.
Report errors about symbols illegal in the programming language.
Screening subtask:
  Identify language keywords and standard identifiers.
  Elimininate "white-spaces", e.g. consecutive blanks and newlines.
  Count line numbers.

## Slide 22: Lexical Analysis (Scanning)

## Slide 23: Syntax Analysis (Parsing)
Input: Sequence of symbols (tokens). Output: Structure of the program:
  concrete syntax tree,
  abstract syntax tree, or
  parse (derivation).
Syntax errors:
  report (as many as possible) syntax errors,
  diagnose syntax errors,
  correct syntax errors.

## Slide 24: Syntax Analysis (Parsing)

## Slide 25: Semantic Analysis
Input: Abstract syntax tree. Output: Abstract syntax tree decorated with attributes, e.g. types of subexpressions.
Report semantic errors, e.g. undeclared variables, type mismatches.
Resolve usage of variables: identify applied occurrences of variables with their declarations.
Compute type of every (sub-)expression.

## Slide 26: Semantic Analysis
1

## Slide 27: Code Selection, Register Allocation, and Instruction Scheduling
c=a+b;
load adr(a)
add
load adr(b)
store adr(c)
Code selection
Instruction scheduling
b
c
a
r1=load adr(a)
r3=add r1, r2
r2=load adr(b)
store adr(c), r3
r1=load adr(a) || r2=load adr(b)
store adr(c), r3
r3=add r1, r2
Register allocation

## Slide 28: Phase Coupling Problem
d1=s1*s1;
d2=s1+s2;
r3=r1*r1
store r3
r3=r1+r2
store r3
r3=r1*r1, r4=r1+r2
store r3
store r4
Optimize number of used registers
Optimize code speed and size

## Slide 29: Main Tasks of Code Generation (1)
Code selection: Map the intermediate representation to a semantically equivalent sequence of machine operations that is as efficient as possible.
Register allocation: Map the values of the intermediate representation to physical registers in order to minimize the number of memory references during program execution.
  Register allocation proper: Decide which variables and expressions of the IR are mapped to registers and which ones are kept in memory.
  Register assignment: Determine the physical registers that are used to store the values that have been previously selected to reside in registers.

## Slide 30: Main Tasks of Code Generation (2)
Instruction scheduling: Reorder the produced operation stream in order to minimize pipeline stalls and exploit the available instruction-level parallelism.
Resource allocation / functional unit binding: Bind operations to machine resources, e.g. functional units or buses.

## Slide 31: Program Representations
Intermediate Representation: typcially the decorated syntax tree, the control flow graph, or the data dependence graph of the input program.

## Slide 32: Program Representations: Call Graph
Call graph:
  There is a node for the main procedure – being the entry node of the program – and a node for each procedure declared in the program.
  The nodes are marked with the procedure names.
  There is an edge between the node for a procedure p to the node of procedure q, if there is a call to q inside of p.

## Slide 33: Program Representations: Control Flow Graph
The control flow graph of a procedure is a directed graph GC=(NC,EC,nA,n) with node and edge labels. For each instruction i of the procedure there is a node ni that is marked by i. The edges (n,m,) denote the control flow of the procedure:   {T,F,} is the edge label. The nodes for composed statements are shown on the next slide. Edges belonging to unconditional branches lead from the node of the branch to the branch destination. The node nA is the uniquely determined entry point in the procedure; it belongs to the first instruction to be executed. n denotes the end node that is reached by any path through the control flow graph.
Nodes with more than one predecessor are called joins and nodes with more than one successor are called forks.

## Slide 34: Control Flow Graph – Composed Statements

## Slide 35: Program Representations: Basic Block Graph & Call Graph
A basic block in a control flow graph is a path of maximal length which has no joins except at the beginning and no forks except possibly at the end.
The basic block graph GB=(NB,EB,bA,b) of a control flow graph GC=(NC,EC,nA,n) is formed from GC by combining each basic block into a node. Edges of GC leading into the first node of a basic block lead to the node of that basic block in GB. Edges of GC leaving the last node of a basic block lead out of the node of that basic block in GB. The node bA denotes the uniquely determined entry block of the procedure; b denotes the exit block that is reached at the end of any path through the procedure.

## Slide 36: Program Representations: Data Dependence Graph
Let GC be a control flow graph. It data dependence graph is a directed graph GD=(ND,ED) with node and edge labels whose nodes are labeled by the operations of the procedure. An edge runs from the node of an operation i to the node of an operation j, if i has to be executed before j, i.e. if there is a path from i to j in the control flow graph and if
  i defines a resource r, j uses it and the path from i to j does not contain other definitions of r (true dependence, RAW): (i,j,r,t)  ED
  i uses a resource, j defines it and the path from i to j does not contain any definitions of r (anti dependence, WAR): (i,j,r,a)  ED
  i and j define the same resource and the path from i to j does not contain any uses nor definitions of r (output dependence, WAR): (i,j,r,o)  ED.

## Slide 37: Life Range and Register Interference
A symbolic register (a variable) r is live at a program point p, if there is a program path from the entry node of the procedure to p that contains a definition of r and there is a path from p to a use of r on which r is not defined. The life range of a symbolic register r is the set of program points at which r is live.
Two life ranges of symbolic registers interfere, if one of them is defined during the life range of the other. The register interference graph is an undirected graph whose nodes are life ranges of symbolic registers and whose edges connect the nodes of interfering life ranges.

## Slide 38: Life Range and Register Interference

## Slide 39: Standard Algorithms for Code Generation
Code selection by tree parsing.
Register allocation by graph coloring.
Instruction scheduling by
  list scheduling
  trace scheduling.
Optimal algorithms for integrated code selection and register allocation for expression trees and special machine models.

## Slide 40: Code Selection

## Slide 41: Impact of Code Selection
struct {
unsigned b1:1;
unsigned b2:1;
unsigned b3:1;
} s;
s.b3 = s.b1 && s.b2;
ld.bu d5, [sp]48
extr.u d5, d5, #0, #1
ne d5, d5, #0
mov16 d4, d5
jeq d4, #0, _9
ld.bu d4, [sp]48
extr.u d4, d4, #1, #1
ne d4, d4, #0
_9:
ld.b d3, [sp]48
insert d3, d3, d4, #2, #1
st.b [sp]48, d3
9 cycles, 42 bytes
ld.bu d5, [sp]48
and.t d3, d5, #0, d5, #1
insert d5, d5, d3, #2, #1
st.b [sp]48, d5
3 cycles, 16 bytes

## Slide 42: Generating Code Selectors
Machine grammar: regular tree grammar;
  terminals: operators from the program representation
  non-terminals: represent storage resources
  often ambiguous
  each rule has associated costs
  factorization, e.g. of addressing modes reduces size.
DREG
AREG
IREG
plus
plus
bconst
m

## Slide 43: Generating Code Selectors
A machine grammar enables IR trees for expressions to be derived. The derivation tree for an IR tree represents one possibility of generating code for the IR tree.
The generated code selector
  parses intermediate representations of programs
  computes derivations according to the machine grammar, each corresponding to a sequence of machine instructions
  has to select a cheapest derivation, corresponding to the (locally) cheapest code sequence
  may compute costs in states or use dynamic programming