## Slide 1: Timing-Predictability of Cache Replacement Policies
Jan Reineke - Daniel Grund
Christoph Berg - Reinhard Wilhelm
AVACS Virtual Seminar, January 12th 2007
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAA

## Slide 2: Predictability in Timing Context
Hard real-time systems
  Strict timing constraints
  Need to derive upper bounds on WCET
time
distribution
{W|A}CET = {Worst|Average}-Case Execution Time
Predictability
Notes: Upper bounds on WCET -> for scheduling analysis -> can all critical tasks be executed?
Copy this slide to position 2? To get the whole talk going…

## Slide 3: Outlook
Caches
Static Cache Analysis
Predictability Metrics for Cache Replacement Policies
Further Predictability Results
Conclusion
Future Work
Notes: Broad audience -> what are caches?
How to derive safe upper bounds -> static cache analysis
Core of the talk -> predictability metrics (how suitable is a cache replacement policy for proving tight upper bounds)
Some more results
Future Work based on the results and on the shortcomings

## Slide 4: Caches: Fast Memory on Chip
Caches are used, because
  Fast main memory is too expensive
  The speed gap between CPU and memory is too large and increasing
Caches work well in the average case:
  Programs access data locally (spatial locality)
  Programs reuse items (temporal locality)
 | Speed | Size
Registers | 0.25 ns | 500 bytes
Cache | 1 ns | 64 KB
Main memory | 100 ns | 512 MB
Hard disk | 5 ms | 100 GB
Notes: Caches have a huge impact on the timing behaviour of a task -> very important for timing analysis

## Slide 5: A-Way Set-Associative Caches
Tag | Index | Block offset
Address:
Tag | Data
Cache Sets:
Tag | Data
…
1
A
=?
Mux
Yes:
Hit!
No:
Miss!
Notes: What happens on a memory access?
Find out whether element is contained in the cache
If so, retrieve it.
If not, fetch it from main memory.
1. Why not fully-associative? -> too expensive, too many comparisons, determination of cache hit would take too long + update logic more expensive as well
2. Usually, cache sets are independent of each other -> can analyze cache sets independently
3. Spatial locality (load lines not single bytes)
4. Temporal locality (-> replacement policy on hits and misses)

## Slide 6: Example: 4-way LRU-Set
z
y
x
t
LRU = Least Recently Used
s
z
y
x
LRU has a
notion of Age
young
old
Age
Miss on s
y
s
z
x
Hit on y
Notes: Why is this a good idea? Rationale of LRU replacement: An element that has recently been accessed is more likely to be accessed in the future -> we want to keep it!
Closing: this should give you an idea of how caches work!

## Slide 7: Cache Analysis: 4-way LRU
Goal: classify accesses as hits or misses
Usually two analyses:
  May-Analysis:
  For each program point (and calling context): Which lines may be in the cache?
     classify misses
  Must-Analysis
  For each program point (and calling context): Which lines must be in the cache?
     classify hits
Notes: Data-Flow Analysis over Control-Flow Graph: Transfer functions + Join Operator
So how does an analysis for LRU look like?

## Slide 8: Must-Analysis for 4-way LRU: Transfer
Which lines must be in the cache?
abstract domain bounds maximal age
{x}
{}
{s,t}
{y}
{s}
{x}
{t}
{y}
Access of s:
young
old
Age
Notes: Concrete cache states represented by the two abstract states?

## Slide 9: Must-Analysis for 4-way LRU: Join
How to combine information at control-flow joins?
{x}
{}
{s,t}
{y}
{s}
{z}
{x}
{y}
young
old
Age
{}
{}
{s,x}
{y}
„Intersection
+ maximal age“
Notes: …
Now that you have a rough idea of cache analysis we can come back to the real topic of the talk: predictability of cache replacement policies

## Slide 10: Predictability in Timing Context
Hard real-time systems
  Strict timing constraints
  Need to derive upper bounds on WCET
time
distribution
{W|A}CET = {Worst|Average}-Case Execution Time
Notes: What are uncertainty and penalty in the context of caches? Cannot classify something as a hit or a miss -> need to assume miss and pay with cache miss penalty.
Penalty is (more or less) independent of replacement policy -> Focus on Uncertainty
Upper bounds on WCET -> for scheduling analysis -> can all critical tasks be executed?

## Slide 11: Uncertainty in Cache Analysis
Notes: There are several reasons for uncertainty: …
Loss of information, introduction of uncertainty, independent of replacement policy…
… to capture the speed of recovery we have defined two metrics  this is were the cache replacement policy comes into play!

## Slide 12: Metrics of Predictability:
Two Variants: M = Misses Only HM = Hits & Misses
evict & fill
[d,c,x]
Notes: If we start out from complete uncertainty: how a long a sequence of accesses do we need to observer until we reach a state that is completely known?
How long does it take until the cache set may only contain elements from the sequence, that is all unknown contents have been eliminated?

## Slide 13: Meaning of evict/fill - I
Evict:
  When do we gain any may-information?
  Safe information about Cache Misses
Fill: must-information:
  When do we gain precise must-information?
  Safe information about Cache Hits

## Slide 14: Meaning of evict/fill - II
Metrics are independent of analyses:
evict/fill bound the precision of any static analysis!
Allows to analyze an analysis:
  Is it as precise as it gets w.r.t. the metrics?

## Slide 15: Replacement Policies
LRU – Least Recently Used
  Intel Pentium, MIPS 24K/34K
FIFO – First-In First-Out (Round-robin)
  Intel XScale, ARM9, ARM11
PLRU – Pseudo-LRU
Intel Pentium II+III+IV, PowerPC 75x
MRU – Most Recently Used

## Slide 16: LRU - Least Recently Used
LRU is the simplest case:
After i ≤ k (associativity) we have exact must-information for i elements.
{}
{}
{}
{}
{a}
{}
{}
{}
{c}
{b}
{a}
{}
{d}
{c}
{b}
{a}
{b}
{a}
{}
{}
 evict(k) = fill(k) = k
a
b
c
d

## Slide 17: FIFO – First-In First-Out
Like LRU in the miss-case
But hits do not change the state
x
c
y
z
a
x
c
y
b
a
x
c
d
b
a
x
b
a
x
c
a
b
c
d

## Slide 18: MRU - Most Recently Used
MRU-bit records whether line was recently used
Problem: never stabilizes
,e
Notes: Name is misleading: It does not replace the most-recently-used element as you might expect.

## Slide 19: Pseudo-LRU
Tree maintains order:
Problem: accesses „rejuvenate“ neighborhood
c
e

## Slide 20: Results: tight bounds
Parametric examples prove tightness.
Notes: Welche Reihenfolge? Konsequenzen der Zahlen wiederholen, z.B. instruction cache, straight-line code, wieviele zeilen um gesicherte may-information zu haben?

## Slide 21: Results: instances for k=4,8
Question: 8-way PLRU cache, 4 instructions per line Assume equal distribution of instructions over 256 sets:
How long a straight-line code sequence is needed to obtain precise must-information?

## Slide 22: Can we do something cheaper?
Analyses that reach perfect precision can be very expensive!
Minimum Live-Span (mls): How long does an element at least survive in the cache?
Enables cheap analysis that just keeps track of the last mls accesses.

## Slide 23: Minimum Live-Span - Results
Notes: Explain values for LRU, FIFO, MRU and PLRU
FIFO: Hit to „oldest“ element
MRU: Access of left-most element just before „big bang“
PLRU: Access Path after access 0…0 needs to be turned to 1…

## Slide 24: Evolution of may/must-information
8-way LRU:
k

## Slide 25: Evolution of may/must-information
8-way FIFO:
k

## Slide 26: Evolution of may/must-information
8-way MRU:
2k-2
k-1

## Slide 27: Evolution of may/must-information
8-way PLRU:
k

## Slide 28: Conclusion
First analytical results on the predictability of cache replacement policies
LRU is perfect in terms of our predictability metrics
FIFO and MRU are particularly bad, especially considering the evolution of must-information

## Slide 29: Future Work
Find new cache replacement policies
Predictable
Cheap to implement
High (average-case) performance
Notes: LRU is expensive

## Slide 30: Future Work
Analyze cache analyses:
Do they ever recover „perfect“ may/must-information?
If so, within evict/fill accesses?
Develop precise and efficient analyses:
Idea: Remember last evict accesses
Problem: Accesses are not pairwise different in practice (cache hits! ;-))

## Slide 31: Future Work
Simplify access sequences :
  <x y z z>  <x y z> !
  <x z y z>  <x y z> ?
  Works for LRU, not for other policies in general?
  Yields currently leading LRU analysis after additional abstraction.

## Slide 32: Future Work
Beyond evict/fill:
Evict/fill assume complete uncertainty
What if there is only partial uncertainty?
Other useful metrics?
Notes: TODO: possibly not assuming pairwise different accesses

## Slide 33: The End

## Slide 34: Caches: How they work
Assume an access to a, cases:
Block m containing a in the cache (hit): request for a is served in the next cycle
Block m not in the cache (miss): m is transferred from main memory to the cache, m may replace some block in the cache,
Replacement policies: LRU, PLRU, FIFO, ... determine how to update the state of the cache upon an access, especially which line to replace

## Slide 35: Results: tight bounds