## Slide 1: A Definition and Classification of Timing Anomalies
Jan Reineke, Björn Wachter, Stephan Thesing, Reinhard Wilhelm
Saarland University
Ilia Polian, Jochen Eisinger, Bernd Becker
University of Freiburg
6th Intl WORKSHOP ON WCET ANALYSIS
Dresden, Germany, July 4, 2006

## Slide 2: Structure
What are Timing Anomalies?
What is the problem?
Related Work
Definition
Classification

## Slide 3: Timing Anomalies – Example 1
Counterintuitive timing behaviour:
  Local worst-case does not entail global worst-case
Notes: Most existing definitions can only deal with this kind of timing anomaly.

## Slide 4: Timing Anomalies – Example 2
Counterintuitive timing behaviour:
  Local worst-case does not entail global worst-case

## Slide 5: What is the problem?
It makes timing analysis more difficult:
  The analysis has to follow all possibilities
  -> exponential blow-up
Goal:
  Prove the absence of timing anomalies
  Identify conditions for safe local decisions
  Need a sound & general definition!

## Slide 6: Related Work
Giving examples, informal description
  Lundqvist & Stenström, `99, `02
  Engblom & Jonsson, `02
  Schneider, `02
  Thesing, `04
Scheduling Anomalies
  Graham, `69
Necessary condition
  Wenzel, Kirner, Puschner, & Riedel, `03, `05
  Limited scope due to underlying assumption
Notes: Level: Observations. No reasons.
Wenzel: schließt spekulations-anomalien aus, sonst weglassen. Vorbereitung.

## Slide 7: Aspects for Definition
Hardware Model
  cycle-level behaviour of machine running a program
Abstraction
  introduces non-determinism
Locality
  what is a local worst-case?
  previously ad hoc: cache hit vs. cache miss
Notes: Reihenfolge, erst Hardware Model.

## Slide 8: Hardware Model + Abstraction
Do not model abstraction explicitly:
  Hardware Model = Maps program to transition system + set of locality constraints
Remark: possible to define correctness condition for abstract model

## Slide 9: Locality
Locality Constraints:
Local worst-case paths?
Locality Constraints for Micro Operations (IF, M, EX, WB, etc.)

## Slide 10: Correspondence of Paths
Compare „related“ paths only: use Locality Constraints

## Slide 11: Definition: Timing Anomalies

## Slide 12: Future Work
Investigate applicability of definition
  Automatically identify Timing Anomalies
  Prove absence under certain conditions (maybe restricted set of locality constraints)
Abstract VHDL model
  Equivalent problem formulation for model checker

## Slide 13: Classification
Scheduling Anomalies
Speculation Anomalies
Cache Anomalies